## Slide 1
WIREFRAME: Supporting Data-dependent Parallelism through Dependency Graph Execution in GPUs
AmirAli Abdolrashidi†, Devashree Tripathy†, Mehmet Esat Belviranli‡,
Laxmi Narayan Bhuyan†, Daniel Wong†
†University of California Riverside
‡Oak Ridge National Research Lab

## Slide 2: Outline
Introduction
Wireframe
DATS: Dependency-Aware TB Scheduler
Evaluation
Conclusion

## Slide 3: Introduction
Since 2007, CUDA allows general-purpose programming for GPUs.

## Slide 4: Introduction
Despite the support for parallelism, GPUs lack support for data-dependent parallelism.
No prior work has provided a generalized solution to inter-block data dependencies.

## Slide 5: CUDA Code Example
Global Barriers (Original)
Sample Wavefront Pattern
int main() {
for (int i=0; i<nWaves; i++) {
kernel<<<GridSize, BlockSize>>>(args);
cudaDeviceSynchronize();
}
}
__global__ void kernel(args) {
processWave();
}
Enormous host-side kernel launch overhead!
Additional delay per TB execution
Notes: e.g. Node 10 could execute considering nodes 9 and 6 are done. But it has to wait for 12 and 3 as well!

## Slide 6: CUDA Code Example
CUDA Dynamic Parallelism (CDP)
int main() {
kernel<<<GridSize, BlockSize>>>(0, args);
cudaDeviceSynchronize();
}
__global__ void kernel(i, args) {
if(i == nWaves) return;
processWave();
if(threadIdx == 0) {
kernel<<<GridSize,BlockSize>>>(i+1,args);
cudaDeviceSynchronize();
}
syncthreads();
}
Kernel Execution Pattern

## Slide 7: CUDA Code Example
CUDA Dynamic Parallelism (CDP)
No more host-side kernel launch
  Device-side launches faster
Support for inter-block parallelism
Spawning depth limit
  24 levels
int main() {
kernel<<<GridSize, BlockSize>>>(0, args);
cudaDeviceSynchronize();
}
__global__ void kernel(i, args) {
if(i == nWaves) return;
processWave();
if(threadIdx == 0) {
kernel<<<GridSize,BlockSize>>>(i+1,args);
cudaDeviceSynchronize();
}
syncthreads();
}

## Slide 8: CUDA Code Example
CDP (Nested)
int main() {
parentKernel<<<GridSize, BlockSize>>>(0, args);
cudaDeviceSynchronize();
}
__global__ void parentKernel(i, args) {
for (int i=0; i<nWaves; i++) {
if(threadIdx == 0) {
childKernel<<<GridSize, BlockSize>>>(args);
cudaDeviceSynchronize();
}
syncthreads();
}
}
__global__ void childKernel(args) {
processWave();
}
Kernel Execution Pattern

## Slide 9: CUDA Code Example
CDP (Nested)
Spawning depth is no more a constraint
The device-side kernel launch still has significant overhead
int main() {
parentKernel<<<GridSize, BlockSize>>>(0, args);
cudaDeviceSynchronize();
}
__global__ void parentKernel(i, args) {
for (int i=0; i<nWaves; i++) {
if(threadIdx == 0) {
childKernel<<<GridSize, BlockSize>>>(args);
cudaDeviceSynchronize();
}
syncthreads();
}
}
__global__ void childKernel(args) {
processWave();
}

## Slide 10: Motivation
There is a need for a generalized support for finer-grain inter-block data dependency for more performance and efficiency.

## Slide 11: Motivation
Current limitations
  High device-side kernel launch overhead
  No general inter-block data dependency support
Our solution: Wireframe
  Hybrid HW/SW solution
    Hardware support for dependent parallelism
    Thread block scheduling
    Programming model
  Main focus is inter-block dependencies

## Slide 12: Wireframe Overview
Host (CPU)
Device (GPU)
Notes: Notes:
Renaming:
Used as reference in the thread block scheduler
Helps minimize used memory size by minimizing the level range between dependent nodes. -> Maximizing the number of nodes cached in hardware
No? -> Large CSR Range -> Inefficient caching!
Key challenges:
Efficient caching -> Solved by HW technique DGB
Efficient scheduling -> LVL bound scheduling

## Slide 13: Dependency Graph
-Stored in compressed sparse (CSR) format
-(Thread block  Node)
-
-Parent count and level of every node determined at runtime
-Sent to the GPU’s global memory

## Slide 14: Node Renaming
During CSR conversion
To minimize data level range in cache

## Slide 15: Programming Model
New functions are needed to support dependency in CUDA
  Add parent
  SM assignment policy selection
Proposing DepLinks model
  Would assign a dependency graph generation function to a kernel
  Easy to learn and use
    Less burden on the programmer

## Slide 16: Code Comparison
DepLinks (Wireframe)
#define parent1 dim3 (blockIdx.x-1, blockIdx.y, blockIdx.z);
#define parent2 dim3 (blockIdx.x, blockIdx.y-1, blockIdx.z);
void* DepLink() {
if (blockIdx.x > 0) WF::AddDependency(parent1);
if (blockIdx.y > 0) WF::AddDependency(parent2);
}
int main() {
kernel<<<GridSize, BlockSize, DepLink>>>(0, args);
cudaDeviceSynchronize();
}
__WF__ void kernel(args) {
processWave();
}
One kernel launch!
parent1
parent2
Notes: DepLinks can be used to create barrier primitives.

## Slide 17: Outline
Introduction
Wireframe
DATS: Dependency-Aware TB Scheduler
Evaluation
Conclusion

## Slide 18: Dependency-Aware TB Scheduler (DATS)
Thread block scheduler
  Issues the relevant thread block at the time for execution based on the dependency graph
Dependency Graph Buffer (DGB)
  Cache data from global memory
  Challenge: Efficient caching and data utilization

## Slide 19: DATS Overview
0
2
4
6
7
9
11
12
14
1
2
3
4
4
5
6
6
7
7
8
9
8
9
9
Global Node Array
Global
Edge Array
GLOBAL MEMORY
Global Edge Start
Global Node ID
0
1
2
3
4
5
6
7
8
9
10
11
13
12
14
0
1
2
3
4
5
6
7
8
Edge Start
Global
NodeID
Parent
Counter
Level
32 bits
16 bits
16 bits
16 bits
Base
Pointer
Translation of Global Edge Start to Local Edge Start
0
2
3
4
0
1
2
3
6
7
7
8
8
5
6
DEPENDENCY GRAPH BUFFER (DGB)
Local Node Array
Local Edge Array
Local Edge Start
Global Node ID
H
0
1
2
3
4
5
6
Pending Update Buffer
Node Insertion Buffer
(Too slow)
(Circular buffer)
7
9
11
12
Global ID
Edge index
Global Edge Start
Node index
Global ID
Edge index
Local Edge Start
Node index

## Slide 20: Dependency Graph Buffer
State | R | W | W | W
Parent Count | 0 | 1 | 1 | 1
Level | 0 | 1 | 1 | 2
Global Node ID | 0 | 1 | 2 | 3
States:
Wait
Ready
Processing
Done
0 | 2 | 4 | 6
1 | 2 | 3 | 4 | 4 | 5 | 6
T
H
Tail
Head
Local Edge Start
Global Node ID
Local Node Array
Local Edge Array

## Slide 21: Example: Child Node Execution
State | R | W | W | W
Parent Count | 0 | 1 | 1 | 1
Level | 0 | 1 | 1 | 2
Global Node ID | 0 | 1 | 2 | 3
States:
Wait
Ready
Processing
Done
1 | 2 | 3 | 4 | 4 | 5 | 6
T
H
0
2
4
6
1
2
2
3
3
R
R
0
0
D
4
1

## Slide 22: Example: Update Buffer Store
State | D | P | P | W
Parent Count | 0 | 0 | 0 | 1
Level | 0 | 1 | 1 | 2
Global Node ID | 0 | 1 | 2 | 3
States:
Wait
Ready
Processing
Done
1 | 2 | 3 | 4 | 4 | 5 | 6
T
H
0
2
4
6
1
2
#4
#5
D
2
Pending Update Buffer
1

## Slide 23: Example: Invalidation…
State | D | P | D | W
Parent Count | 0 | 0 | 0 | 1
Level | 0 | 1 | 1 | 2
Global Node ID | 0 | 1 | 2 | 3
States:
Wait
Ready
Processing
Done
1 | 2 | 3 | 4 | 4 | 5 | 6
T
H
0
2
4
6
#4
#5
#4
Enough spaces to load to DGB
1
2
3
R
0
4
5
D

## Slide 24: Example: …Reloading data
State | W | W | D | R
Parent Count | 2 | 1 | 0 | 0
Level | 2 | 2 | 1 | 2
Global Node ID | 4 | 5 | 2 | 3
States:
Wait
Ready
Processing
Done
6 | 7 | 7 | - | - | - | 6
T
H
0
2
-
6
#4
#5
#4
Load complete!
6

## Slide 25: Example: Update Buffer Load
State | W | W | D | P
Parent Count | 2 | 1 | 0 | 0
Level | 2 | 2 | 1 | 2
Global Node ID | 4 | 5 | 2 | 3
States:
Wait
Ready
Processing
Done
6 | 7 | 7 | - | - | - | 6
T
H
0
2
-
6
#4
#5
#4
1
3
4
1
0
2
R
0
R

## Slide 26: Level Range
Imbalanced execution may entail using the baseline TB scheduling policy (LRR).
More level range means:
-Larger DGB is required
-Might limit CTA execution
Key challenge:
Efficient scheduling

## Slide 27: Level-bound Scheduling (LVL)
Prioritizing lower-level thread blocks in the graph
More ready nodes  More parallelism
Minimizing the caching operation
Limiting the level range to avoid serialization

## Slide 28: Outline
Introduction
Wireframe
DATS: Dependency-Aware TB Scheduler
Evaluation
Conclusion

## Slide 29: Evaluation
Evaluation platform
  GPGPU-Sim v3.2.2 (GTX480)
  Six modified benchmarks to actively make use of data dependency
    HEAT2D, IMG_INT, DTW
    HIST, SOR, SW
Cases
  Global, CDP
  DepLinks primitives
  LRR and LVL
    LVL=3
Notes: DepLinks: Replaced global barriers with our dependency graph primitives (LVL=0)

## Slide 30: Local Node Array Size
Empirical estimation used
Minimum size chosen (128 entries)
Notes: Empirical estimation

## Slide 31: Local Edge Array Size

## Slide 32: Evaluation
2KB area overhead
No significant impact on L2 miss rate
Low memory request overhead
  0.13% Average
Performance improvement
  45% average improvement

## Slide 33: Computations vs Launch Overhead
With a constant data size
  Kernel launches increase
is still sizable at 9K nodes.
  times on average
Chart: Comp/Launch Ratio
| DTW | HEAT2D | HIST | INT_IMG | SOR | SW | GeoMean
1K | 7.6302 | 11.9336 | 5.946 | 5.8868 | 12.2385 | 7.8903 | 8.2168
4K | 4.689 | 5.5318 | 2.9451 | 3.1665 | 5.6778 | 4.1944 | 4.234
9K | 3.8465 | 4.0862 | 2.1402 | 1.9447 | 4.31 | 3.2393 | 3.1149

## Slide 34: Performance
Impact on L2 ~ 0.5%

## Slide 35: Performance Breakdown
(Graph size = 4K)
Chart: 
| DTW | HEAT2D | HIST | INT_IMG | SOR | SW | GeoMean
LVL | 1.2979 | 1.2963 | 1.3502 | 1.3649 | 1.2863 | 1.297 | 1.3151
LRR | 1.2532 | 1.2688 | 1.3651 | 1.356 | 1.2557 | 1.2754 | 1.2949
DepLinks | 1.2104 | 1.2005 | 1.316 | 1.3298 | 1.1977 | 1.2352 | 1.2471
CDP | 1.0617 | 1.0533 | 1.0914 | 1.0861 | 1.052 | 1.0679 | 1.0686
Global | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 36: Performance
Chart: Overall Speedup (LVL)
| DTW | HEAT2D | HIST | INT_IMG | SOR | SW | GeoMean
1K | 1.1451 | 1.0984 | 1.1725 | 1.1754 | 1.0965 | 1.1446 | 1.1383
4K | 1.2979 | 1.2963 | 1.3502 | 1.3649 | 1.2863 | 1.297 | 1.3151
9K | 1.3948 | 1.4105 | 1.3658 | 1.652 | 1.4079 | 1.4735 | 1.4478
Speedup across different graph sizes
+45%
+65%

## Slide 37: Conclusion
Supporting generalized inter-block dependencies through hardware
Minimizing caching through level-bound TB scheduling
45% average improvement over the baseline

## Slide 38: Conclusion
Future Work
  More policies regarding the locality/load balance for SMs
  Dynamic dependency
    Ability to run workloads with variable sizes, e.g. BFS
  Automation/optimization of the graph generation by the compiler
    No more load on the programmer!

## Slide 39: Thank you!
Questions?

## Slide 40: Performance (IPC)

## Slide 41: LVL vs LRR

## Slide 42: DepLinks Synchronization Primitives

## Slide 43: Thank you!
Questions?